## Slide 1: “The IAEA Global Network of Isotopes in Precipitation (GNIP) – Overview”
Stefan Terzer
Isotope Hydrology Section
International Atomic Energy Agency
Vienna, Austria

## Slide 2: GNIP objectives
Systematic collection of basic data on isotopic content in precipitation (monthly basis)
on a global scale to determine temporal and spatial variations
of environmental isotopes in precipitation.

## Slide 3: GNIP history
Founded 1961, collaboration IAEA-WMO
  Focus: Monitoring of thermonuclear fallout
Reduction in 1975, national networks est.
  Focus: Isotope Hydrology
Clients from new fields:
  Climate change + AGCMs (since 1990s), Ecology, forensics etc. (since 2000s)

## Slide 4: Station count timeline
Chart: 
| 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
GNIP total | 96 | 138 | 152 | 160 | 204 | 209 | 188 | 185 | 183 | 175 | 170 | 175 | 184 | 178 | 194 | 177 | 167 | 181 | 176 | 186 | 184 | 193 | 203 | 199 | 195 | 209 | 184 | 207 | 245 | 282 | 229 | 235 | 215 | 186 | 207 | 215 | 234 | 248 | 234 | 278 | 276 | 299 | 293 | 249 | 204 | 221 | 191 | 185 | 162 | 161 | 141 | 199 | 224 | 282
GNIP Stable Is. | 54 | 90 | 90 | 100 | 115 | 108 | 99 | 111 | 99 | 92 | 92 | 119 | 133 | 124 | 140 | 124 | 113 | 123 | 120 | 135 | 132 | 145 | 158 | 151 | 151 | 170 | 151 | 176 | 216 | 257 | 207 | 215 | 191 | 166 | 193 | 203 | 223 | 236 | 222 | 267 | 266 | 290 | 286 | 242 | 197 | 198 | 169 | 180 | 158 | 158 | 139 | 197 | 222 | 280
GNIP Tritium | 81 | 119 | 140 | 150 | 194 | 202 | 178 | 178 | 171 | 172 | 166 | 163 | 166 | 160 | 162 | 151 | 135 | 150 | 150 | 162 | 176 | 177 | 155 | 154 | 148 | 165 | 161 | 175 | 185 | 202 | 175 | 176 | 152 | 119 | 138 | 106 | 128 | 117 | 114 | 146 | 125 | 117 | 101 | 110 | 100 | 121 | 112 | 101 | 98 | 83 | 61 | 103 | 105 | 107

## Slide 5: GNIP network coverage (2013)

## Slide 6: GNIP sample collection
Representative of local precipitation
  Rain gauge siting
  Completeness over the year: no gaps, no overflows
Evaporation prevention
  During collection
  and storage

## Slide 7: Collection devices
Standard rain gauge (manual accumulation)
Submerged-tube totalizer
Paraffin oil based totalizer
Table tennis ball totalizer

## Slide 8: GNIP structure
Core stations situated in climatically relevant locations
  Operated by weather services, analysis @ IAEA
National networks composed of stations operated by national authorities
  E.g. Germany, Switzerland, Spain
Affiliated stations which are stations resulting from studies (short-term in nature)

## Slide 9: IAEA & GNIP (I)
IAEA support for GNIP stations includes
  Provision of bottles and sampling instructions
  Samples shipped 1-2x/year
  Analytical services, usually @ IAEA-IHL

## Slide 10: IAEA & GNIP (II)
R&D, Testing, QA/QC
  Rain sampling devices
  Laser Spectroscopy, Tritium analysis
  Interlaboratory comparison
GNIP Database
  Data compilation
  Dissemination

## Slide 11: GNIP data - attributes
Organization by sampling frequency
  GNIP – monthly (monthly composite samples)
  GNIP – Events (with resolution > monthly)
Parameters recorded
  Isotopic composition (δ2H, δ18O, some also 3H)
  Meteorological attributes (precip type, amount, air temperature and vapour pressure)

## Slide 12: GNIP known issues (I)
Coverage-related
  Uneven spatial coverage of stations
  Need for data in remote areas
  Partial or incomplete isotope and/or meteorological records
Organizational
  Collaboration on voluntary basis
  New users and coordination of new contributors

## Slide 13: GNIP known issues (II)
Organizational (contd.)
  Awareness of weather services
  Automatization of weather stations
  Sampling/storage protocols compliance
  Data QA/QC from externally contributing labs
  Data ownership issues

## Slide 14: GNIP recent materials

## Slide 15: RCWIP - an improved global water isotope pattern prediction model using fuzzy climatic clustering regionalization
S. Terzer, L.I. Wassenaar,
L. Araguas-Araguas and P.K. Aggarwal
Isotope Hydrology Section
International Atomic Energy Agency
Vienna, Austria

## Slide 16: Isoscapes
Gridded precipitation δ18O and δ2H prediction data from GNIP (& related) data
Increasing demand by hydrology, meteorology, climatology, ecology and forensics
1st regression-interpolation model by Bowen et al. (BW, 2002, 2003)
  δ18O = f (Lat2, abs(Lat), Alt) + Interpolation

## Slide 17: Workflow: BW
Station data (i)
Latitude/Longitude
Elevation
Preliminary estimate
Station residual
Interpolation
Regression estimate
for each grid cell
using
DEM
Latitude/Longitude
Elevation
Final estimate

## Slide 18: Regression-Interpolation Models
Global parameterization
  Best-suited regressor combination (Bowen 2010)
Vs. regional fitting
  Austria (Liebminger et al. 2006)
  Mediterranean (Lykoudis & Argiriou 2007)
  China (Lui et al. 2008)
  Mexico (Wassenaar et al. 2009)
Global coverage but
poorer local predictions
Better fit but
limited domain

## Slide 19: RCWIP – bridging the gap
Regionalization: Formation of climatically similar subsets of GNIP stations
Cluster-specific best-fit regressors
  For each cluster and month
Summing and weighting
  According to membership fractions

## Slide 20: Workflow: BW  RCWIP
Station data (i)
Latitude/Longitude
Elevation
Preliminary estimate
Station residual
Interpolation
Regression estimate
for each grid cell
using
DEM
Latitude/Longitude
Elevation
Subset A ()
Subset B ()
m subsets ()
m regression equations ()
Subset B ()
Subset A ()
m subsets ()
using
using
using
Final estimate
Station residual
Regression
Estimate
Climate Data
Gridded Clim. Data
Fuzzy
Clustering
Best-fit regr.
choice
Fuzzy
Clustering
Best-fit regr.
choice

## Slide 21: Fuzzy clustering (1)
  Fuzzy c-means clustering (Bezdek et al. 1981 etc.) created 36 climatic clusters
  No crisp cluster boundaries, membership fractions between 0 and 1
  E.g. Athens
Cluster 12
0.52
Cluster 10
0.34
Cluster 4
0.00
Cluster 2
0.00
Cluster 1
0.14

## Slide 22: Fuzzy clustering - Results

## Slide 23: RCWIM – Regressions
Cluster-specific best-fit regressors
  For each cluster and month (also annual)
  Possible covariates: Lat, Long, Alt, Precipitation amount, Air temperature, Vapour pressure, precipitable water
  Combination obtainng highest R2 chosen
  If no regression possible, supplemented by global best fit model

## Slide 24: Regression results
Lower regression residuals
  Improvement of prediction for 67% of stations
  RMSE lower for any cluster-month
    Example: Cluster 10 („Rabat/Kenitra“)
Chart: 
| -5 | -4.5 | -4 | -3.5 | -3 | -2.5 | -2 | -1.5 | -1 | -0.5 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
 | 1 | 2 | 4 | 4 | 15 | 16 | 17 | 40 | 73 | 109 | 138 | 133 | 39 | 12 | 7 | 5 | 1 | 5 | 0 | 0 | 0
Chart: Month
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Precip | 86.1 | 76.8 | 57.3 | 46.3 | 29.1 | 9.4 | 0.3 | 4.3 | 10.1 | 47.3 | 96.3 | 112.4
M1 RMSE | 1.3163 | 1.3398 | 1.2298 | 1.1973 | 0.96816 | 1.1523 | 1.6284 | 1.3703 | 1.21 | 1.0175 | 1.2005 | 1.3549
M3 RMSE | 1.8988 | 1.7735 | 2.6052 | 2.472 | 1.8344 | 1.985 | 2.6703 | 2.0419 | 1.862 | 1.2667 | 1.5222 | 1.8216
BW
RCWIM

## Slide 25: Kriging (1)
Improved variograms, lowered sills
  BW for δ18OANN: 4.53 ‰
  RCWIM: 1.93 ‰
Result: Lower Kriging error
  BW for δ18OANN: 1.4 ‰
  RCWIM: 1.0 ‰
Chart: Distance (degrees)
BW
RCWIM

## Slide 26: Kriging (2)
Reduction of δ18OANN standard error particularly over data-scarce areas

## Slide 27: RCWIM Isoscapes – Examples
Predicted Global annual amount weighted δ18O

## Slide 28: RCWIM Isoscapes – examples
Predicted Growing Season amount weighted δ2H

## Slide 29: Isoscapes – Seasonal Predictions
May
Feb
Aug
Nov
Seasonal δ18O

## Slide 30: Conclusion
Combination of regionally specific regression models + residual interpolation to predict monthly and annual δ18O and δ2H.
Spatial Analysis used to predict mean δ18O for upstream catchment area of a point along the river

## Slide 31: Thanks for your attention!
Check for updates:
http://www.iaea.org/water